HEALTH and SAFETY DATA SHEET

Color-Pave Limited, Unit 1 Astra Business Centre, Roman Way Industrial Estate, PRESTON PR2 5AP. Tel 01772 701474

1. IDENTIFICATION OF THE PRODUCT  :

PRODUCT                   CONCRETE SURFACE CLEANER

INTENDED USE            CLEANER FOR CONCRETE

___________________________________________________________________________________________________________

2. COMPOSITION/INFORMATION ON INGREDIENTS:

HAZARDOUS INGREDIENTS             INDEX No         CONTENT           CAS                   R PHRASES

Phosphoric Acid                                 231-595-7            < 10 %                7647-01-1                   R34-3711-20

___________________________________________________________________________________________________________

3.  HAZARDS IDENTIFICATION :

Causes burns. Irritating to respiratory system, high atmospheric concentrations may lead to pulmonary      oedema.

___________________________________________________________________________________________________________

4.  FIRST AID MEASURES :

Exposure Route                                                     Symptom                                                 Treatment

Inhalation                             Coughing ,wheezing, shortness of breath           Remove from exposure, rest and

keep warm. In severe cases, or if  recovery

is not  rapid or complete. Seek   medical

attention.

Skin Contact                          Burns                                                                              Drench the skin with plenty of water.

Remove contaminated

clothing and  wash before  re-use.

If  large areas of

the skin is damaged or if

irritation  persists seek  medical attention.

Eye Contact                           Severe burns may cause permanent                     Irrigate thoroughly with water

damage                                                                          for  at least 10 minutes.

Obtain  medical attention.

Ingestion                                Severe burns to gastrointestinal tract                Wash mouth out with water. Do

do not induce vomiting.

If the patient conscious ,

give water to drink .

If  patient feels unwell

seek medical attention.

__________________________________________________________________________________

5. FIRE FIGHTING MEASURES :

Extinguishing media :

Recommend : Alcohol resistant foam ,Carbon Dioxide , Powder, Water spray.

NOT TO BE USED :  WATER JET

Recommendations :

Hazardous Combustion Products :    none

Special Equipment for Fire Fighting: Self contained breathing apparatus and full protective clothing. _____________________________________________________________________________________________________

6. ACCIDENTAL RELEASE MEASURES :

Safety Precautions :                  Wear appropriate PPE - Section 8

Environmental Precautions: Do not allow undiluted material to enter drains, sewers or water courses.

Clean up Procedures :            Bund spill area, dilute with plenty of water and neutralise with lime slurry

or sodium carbonate. Flush away with plenty of water. _____________________________________________________________________________________________________

7. HANDLING AND STORAGE :

Handling:

Ventilation: Good general ventilation.  Avoid contact with skin and eyes. Do not breathe fumes.

Storage :      Store at ambient temperatures. Store in ,Rubber lined mild steel, PVC, High density polythene.

_____________________________________________________________________________________________________

8. EXPOSURE CONTROL/ PERSONAL PROTECTION:

Exposure Limits                                 5 ppm ( 7mg/m3 ), STEL.

Protective Measures

Respiratory       :                                  Type approved RPE for acidic vapours

Hand                  :                                   PVC or rubber gloves

Eye                      :                                   Safety goggles

Skin                    :                                   Rubber boots, PVC overalls

._____________________________________________________________________________________________________

9. PHYSICAL AND CHEMICAL PROPERTIES:

Physical state:            Liquid                                                                      Vapour Density:           heavier than air

Odour              :            Pungent                                                                   Solubility in water:     completely soluble

Melting Point :           < - 29 o c                                                                     ph       :                       < 1

Relative Density  :      > 1.125 @ 15.5 o c                                                    Flammability    :      Not  combustible           _________________________________________________________________________________________________

10. STABILITY AND REACTIVITY:

Attacks most common metals liberating hydrogen, which can form explosive mixtures with air .

Can react violently with oxidising agents, liberating chlorine.

Avoid contact with Alkalis, concentrated sulphuric  acid ,oxidising agents, ammonia/amines.

_____________________________________________________________________________________________________

11. TOXICOLOGICAL INFORMATION;

Inhalation of mists and vapours will cause irritation of the upper respiratory tract, high concentrations may cause corrosion, pulmonary  oedema may occur up to 48 hours after exposure. Corrosive to skin, eyes, and mucous membranes. Ingestion may cause damage to the gastrointestinal tract. Repeated exposure to low levels may cause erosion of the teeth and ulceration of the nasal septum and gums.

_____________________________________________________________________________________________________

12. ECOLOGICAL INFORMATION:

Mobility              :                         Highly volatile liquid, soluble in water, predicted to have high mobility in

soil.

Degradability   :                          Neutralised slowly by natural alkalinity.

Bio-accumaulative potential  :   Material does not  bio-accumulate.

Aquatic Toxicity  :                        Fatal to fish and other aquatic life due to low pH.

_____________________________________________________________________________________________________

13 . DISPOSAL CONSIDERATIONS:

Wastes ,including emptied containers are controlled wastes and should be disposed of in accordance

with regulations made under the Control of Pollution Act and the Environment Pollution Act.

_____________________________________________________________________________________________________

14.  TRANSPORT INFORMATION :

For Domestic Road/Rail                Corrosive Liquid                                           UN/S.I. No. 1789

Class:  2R                                             Packing Group   11                                      ADR Class/Item No 8, 5 o (b)

HI  No. 80                                            Transport  category   2R

_____________________________________________________________________________________________________

15. REGULATORY INFORMATION:

Supply label details          Reference CHIP ‘97

Label System                      Phosphoric Acid ......%

Symbols ;                              Corrosive

Risk Phrases  :                   34 - 37    Causes  burns. Irritating to respiratory system.

Safety Phrases   :                26 - 45    In cases of contact with eyes, rinse immediately with plenty of water                                                             and seek medical advise, in case of accident or if you feel unwell seek                                                                         medical advise   immediately (show label where possible).

E.E.C. No                             231-595-7 _____________________________________________________________________________________________________

16.  OTHER INFORMATION :

The information contained in this safety data sheet is provided in accordance with the requirements of the Chemicals (Hazard Information and Packaging ) Regulations.

The product should not be used for purposes other than those shown in Section 1 without first  referring to the supplier and obtaining written handling instructions. As the specific conditions of the use of the product are outside the suppliers control ,the user is responsible  for ensuring that the requirements of the relevant legislation are complied  with.

The information contained in this safety data sheet is based on the present state of knowledge and current legislation, It provides guidance on health, safety and environmental aspects of the product  and should not  be construed as any guarantee of technical performance or suitability for particular applications